## Slide 1: CS321: Computer Architecture
Course web:
http://172.16.1.6/~jimson/

## Slide 2: Computer Architecture
Basic functional blocks of a computer: CPU, memory, input-output subsystems, control unit.
Instruction set architecture of a CPU - registers, instruction execution cycle, RTL interpretation of instructions, addressing modes, instruction set. Case study - instruction sets of some common
CPUs; Assembly language programming for some processor; Data representation: signed number
representation, fixed and floating point representations, character representation. Computer
arithmetic - integer addition and subtraction, ripple carry adder, carry look-ahead adder, etc.
multiplication – shift-and-add, Booth multiplier, carry save multiplier, etc. Division - non-restoring and restoring techniques, floating point arithmetic; CPU control unit design: hardwired and microprogrammed design approaches, Case study - design of a simple hypothetical CPU; Pipelining:
Basic concepts of pipelining, throughput and speedup, pipeline hazards; Memory organization:
Memory interleaving, concept of hierarchical memory organization, cache memory, cache size vs
block size, mapping functions, replacement algorithms, write policy; Peripheral devices and their characteristics: Input-output subsystems, I/O transfers - program controlled, interrupt driven and
DMA, privileged and non-privileged instructions, software interrupts and exceptions. Programs
and processes - role of interrupts in process state transitions.

## Slide 3: Prerequisite & Text Book
Prerequisite: CS225 & CS226
Text Books
David A. Patterson, John L. Hennessy, Computer Organization and Design, Fourth Edition:
The Hardware/Software Interface, Morgan Kaufmann; 4 edition, 2011.
2. A. Tenenbaum, Structured Computer Organization, 4th Ed, Prentice-Hall of India, 1999.
3. W. Stallings, Computer Organization and Architecture: Designing for Performance, 6th
Ed, Prentice Hall, 2005.
4. J. Hennessy and D. Patterson, Computer Architecture A Quantitative Approach, 3rd Ed,
Morgan Kaufmann, 2002..

## Slide 4: Evaluation Policy(CS321)
Assignments
& Quizzes : 30%
Mid‐Sem : 15%
End‐Sem : 35%
Mini Project:20 %

## Slide 5: Architecture Lab(CS322)
Regular Lab work, 30%
Mid‐Sem : 15%
End‐Sem : 30%
Mini Project:25 %

## Slide 6: Levels of Transformation
Microarchitecture
ISA (Architecture)
Program/Language
Algorithm
Problem
Logic
Circuits
Runtime System
(VM, OS, MM)
Electrons
“The purpose of computing is insight” (Richard Hamming)
We gain and generate insight by solving problems
How do we ensure problems are solved by electrons?
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Algorithm: step by step procedure where each step is effectively computable, is definite (precisely defined), and terminates

## Slide 7: The Power of Abstraction
Levels of transformation create abstractions
  Abstraction: A higher level only needs to know about the interface to the lower level, not how the lower level is implemented
  E.g., high-level language programmer does not really need to know what the ISA is and how a computer executes instructions
Abstraction improves productivity
  No need to worry about decisions made in underlying levels
  E.g., programming in Java vs. C vs. assembly vs. binary vs. by specifying control signals of each transistor every cycle
Then, why would you want to know what goes on underneath or above?

## Slide 8: Why CS321?
What if
  The program you wrote is running slow?
  The program you wrote does not run correctly?
  The program you wrote consumes too much energy?
What if
  The hardware you designed is too hard to program?
  The hardware you designed is too slow because it does not provide the right primitives to the software?

## Slide 9: An Example: Multi-Core Systems
CORE 1
L2 CACHE 0
SHARED L3 CACHE
DRAM INTERFACE
CORE 0
CORE 2
CORE 3
L2 CACHE 1
L2 CACHE 2
L2 CACHE 3
DRAM BANKS
Multi-Core
Chip
*Die photo credit: AMD Barcelona
DRAM MEMORY CONTROLLER

## Slide 10: Unexpected Slowdowns in Multi-Core
Memory Performance Hog
Low priority
High priority
(Core 0)
(Core 1)
Moscibroda and Mutlu, “Memory performance attacks: Denial of memory service
in multi-core systems,” USENIX Security 2007.
Notes: What kind of performance do we expect when we run two applications on a multi-core system? To answer this question, we performed an experiment. We took two applications we cared about, ran them together on different cores in a dual-core system, and measured their slowdown compared to when each is run alone on the same system. This graph shows the slowdown each app experienced. (DATA explanation…)
Why do we get such a large disparity in the slowdowns?
Is it the priorities? No. We went back and gave high priority to gcc and low priority to matlab. The slowdowns did not change at all. Neither the software or the hardware enforced the priorities.
Is it the contention in the disk? We checked for this possibility, but found that these applications did not have any disk accesses in the steady state. They both fit in the physical memory and therefore did not interfere in the disk.
What is it then? Why do we get such large disparity in slowdowns in a dual core system?
I will call such an application a “memory performance hog”
Now, let me tell you why this disparity in slowdowns happens.
Is it that there are other applications or the OS interfering with gcc, stealing its time quantums? No.

## Slide 11: A Question or Two
Can you figure out why there is a disparity in slowdowns if you do not know how the processor executes the programs?
Can you fix the problem without knowing what is happening “underneath”?

## Slide 12: Why the Disparity in Slowdowns?
CORE 1
CORE 2
L2
CACHE
L2
CACHE
DRAM MEMORY CONTROLLER
DRAM
Bank 0
DRAM
Bank 1
DRAM
Bank 2
Shared DRAM
Memory System
Multi-Core
Chip
unfairness
INTERCONNECT
matlab
gcc
DRAM
Bank 3
Notes: -In a multi-core chip, different cores share some hardware resources. In particular, they share the DRAM memory system. The shared memory system consists of this and that.
When we run matlab on one core, and gcc on another core, both cores generate memory requests to access the DRAM banks. When these requests arrive at the DRAM controller, the controller favors matlab’s requests over gcc’s requests. As a result, matlab can make progress and continues generating memory requests. These requests are again favored by the DRAM controller over gcc’s requests. Therefore, gcc starves waiting for its requests to be serviced in DRAM whereas matlab makes very quick progress as if it were running alone.
Why does this happen? This is because the algorithms employed by the DRAM controller are unfair.
But, why are these algorithms unfair? Why do they unfairly prioritize matlab accesses?
To understand this, we need to understand how a DRAM bank operates.
Almost all systems today contain multi-core chips
Multi-core systems consist of multiple on-chip cores and caches
Cores share the DRAM memory system
DRAM memory system consists of
  DRAM banks that store data (multiple banks to allow parallel accesses)
  DRAM memory controller that mediates between cores and DRAM memory
    It schedules memory operations generated by cores to DRAM
This talk is about exploiting the unfair algorithms in the memory controllers to perform denial of service to running threads
To understand how this happens, we need to know about how each DRAM bank operates

## Slide 13: DRAM Bank Operation
Row Buffer
(Row 0, Column 0)
Row decoder
Column mux
Row address 0
Column address 0
Data
Row 0
Empty
(Row 0, Column 1)
Column address 1
(Row 0, Column 85)
Column address 85
(Row 1, Column 0)
HIT
HIT
Row address 1
Row 1
Column address 0
CONFLICT !
Columns
Rows
Access Address:

## Slide 14
INTRODUCTION

## Slide 15: Generations of Computer
First Generation - 1940-1956: Vacuum Tubes
Second Generation - 1956-1963: Transistors
Third Generation - 1964-1971: Integrated Circuits
Fourth Generation - 1971-Present: Microprocessors
Fifth Generation - Present and Beyond: Artificial Intelligence

## Slide 16: FIRST GENERATION 1940 - 1956
First generation computers used Vacuum Tubes
Vacuum tubes are glass tubes with circuits inside.
The word vacuum indicates that they have no air inside, which protects the circuitry.
Building a computer with these vacuum tubes would result in a very large machine occupying one full room.

## Slide 17: First Transistor
Uses Silicon
developed in 1948
won a Nobel prize
on-off switch
Second Generation Computers used Transistors, starting in 1956

## Slide 18: Integrated Circuits
Third Generation Computers used Integrated Circuits (chips).
Integrated Circuits are transistors, resistors, and capacitors integrated together into a single “chip”
Instead of punched cards and printouts, users started interacting with keyboards and mouse.

## Slide 19: 1972: 8008 Microprocessor
The 8008 was twice as powerful as the 4004.
According to the magazine Radio Electronics, Don Lancaster, a dedicated computer hobbyist, used the 8008 to create a predecessor to the first personal computer, a device Radio Electronics dubbed a "TV typewriter." It was used as a dumb terminal.

## Slide 20: 1978: 8086-8088 Microprocessor
In 1978 intel
  16-bit
  2.5MIPS millions of instructions per second
  1M-byte memory
  4- or 6-byte instruction (cache) queue that prefetch instructions
  over 20,000 variations instructions.
  64K bytes of memory found in 8-bit microprocessors to execute efficiently
  The 16-bit 8086 and 8088 provided 1M byte of memory for these applications
  Popularity of Intel ensured in 1981 when IBM chose the 8088 in its personal computer

## Slide 21: 1982: 286 Microprocessor
The 286, also known as the 80286, was the first Intel processor that could run all the software written for its predecessor.
This software compatibility remains a hallmark of Intel's family of microprocessors.
Within 6 years of it release, there were an estimated 15 million 286-based personal computers installed around the world.
80286: updated 8086
  16M byte memory addressing
  Instructions identical to 8086 few more added
  4MIPS
  8Mhz clock speed

## Slide 22: 1985: Intel 386(TM) Microprocessor
The Intel 386TM microprocessor featured 275,000 transistors--more than 100times as many as the original 4004.
It was a 32-bit chip and was "multi tasking," meaning it could run multiple programs at the same time.
80386 (1985)
  32-bit address bus and 32-bit data bus
  4GB memory
  Hardware circuitry for memory management
  Additional instructions referenced 32-bit registers and managed the memory system

## Slide 23: 1989: Intel 486(TM) DX CPU
The 486TM generation really allowed the shift from command-level computing into point-and-click computing.
The Intel 486TM processor was the first to offer a built-in math coprocessor, which speeds up computing because it offers complex math functions from the central processor.
80486
  Highly integrated package.
  80386-like microprocessor.80387-like numeric coprocessor.
  50 MIPS
  8K-byte cache memory system
  Half of its instructions executed in 1 clock cycle rather 2

## Slide 24: 1993: Pentium® Processor
The Pentium® processor allowed computers to more easily incorporate "real world" data such as speech, sound, handwriting and photographic images.
The name Pentium®, mentioned in the comics and on television talk shows, became a household word soon after introduction.
  Originally named P5 or 80586
  Clock speed of 60MHZ
  Executes 110MIPS
Cache size: 16K bytes (8K cache in 80486)
  8K-byte instruction cache and data cache.
Memory system up to 4G bytes.
Data bus width increased to a full 64 bits.
Data bus transfer speed 60 MHz or 66 MHz.
  depending on the version of the Pentium

## Slide 25: 1995: Pentium® Pro Processor
Released in the fall of 1995 the Pentium® Pro processor is designed to fuel 32-bit server and workstation-level applications, enabling fast computer-aided design, mechanical engineering and scientific computation.
Each Pentium® Pro processor is packaged together with a second speed-enhancing cache memory chip.
The powerful Pentium® Pro processor boasts 5.5 million transistors.

## Slide 26: 1997: Pentium® II Processor
The 7.5 million-transistor Pentium® II processor incorporates Intel MMXTM technology, which is designed specifically to process video, audio and graphics data efficiently.
It is packaged along with a high-speed cache memory chip in an innovative Single Edge Contact (S.E.C.) cartridge that connects to a motherboard via a single edge connector, as opposed to multiple pins.
With this chip, PC users can capture, edit and share digital photos with friends and family via the Internet; edit and add text, music or between-scene transitions to home movies; and, with a video phone, send video over standard phone lines and the Internet.

## Slide 27: Moore’s Law
IC capacity doubling about every 18 months for several decades
  Known as “Moore’s Law” after Gordon Moore, co-founder of Intel
    Predicted in 1965 predicted that components per IC would double roughly every year or so
  Picture depicts related phenomena
    For a particular number of transistors, the IC shrinks by half every 18 months
      Notice how much shrinking occurs in just about 10 years
      Enables incredibly powerful computation in incredibly tiny devices
  Today’s ICs hold billions of transistors
    The first Pentium processor (early 1990s) needed only 3 million

## Slide 28: Moore’s law in Microprocessors
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
P6
0.001
0.01
0.1
1
10
100
1000
1970
1980
1990
2000
2010
Year
Transistors (MT)
2X growth in 1.96 years!
Transistors on Lead Microprocessors double every 2 years
Courtesy, Intel

## Slide 29: Die
Single die
Wafer
From http://www.amd.com
Going up to 12” (30cm)

## Slide 30: In Picture…
Silicon Process Technology
1.5µ 1.0µ 0.8µ 0.6µ 0.35µ 0.25µ 0.18µ 0.13µ
Intel386™ DX Processor
Intel486™ DX Processor
Pentium® Processor
Pentium® Pro Processor
Pentium® II Processor
Pentium® 4 Processor
Pentium® III Processor
Notes: P-III sizes –
0.25u 140 mm^2, 9.5 M trans 0KB L2;
01.8 106 mm^2, 28M Trans, 128KB L2;
01.3 79 mm^2, 40M Trans, 512KB L2
P4P sizes –
W 1.75V 2GHZ 75 Watts 217mm^2 42M trans, 256KB L2
N 1.5V 2GHZ 52W, 2.2GHZ 55W 146mm^2 55M tran 512KB L2

## Slide 31
Number of transistors on an integrated circuit doubles ~ every two years
Image source: Wikipedia

## Slide 32
Courtesy, Intel

## Slide 33
Courtesy, Intel

## Slide 34
Courtesy, Intel

## Slide 35: Power will be a major problem
5KW
18KW
1.5KW
500W
4004
8008
8080
8085
8086
286
386
486
Pentium® proc
0.1
1
10
100
1000
10000
100000
1971
1974
1978
1985
1992
2000
2004
2008
Year
Power (Watts)
Power delivery and dissipation will be prohibitive
Courtesy, Intel

## Slide 36
Courtesy, Intel

## Slide 37
Courtesy, Intel

## Slide 38: This Course
Micro-architecture: how to implement an architecture in hardware
Processor:
  Datapath: functional blocks
  Control: control signals
This Course

## Slide 39: What is Computer Architecture?
The science and art of designing, selecting, and interconnecting hardware components and designing the hardware/software interface to create a computing system that meets functional, performance, energy consumption, cost, and other specific goals.
We will soon distinguish between the terms architecture, and microarchitecture.

## Slide 40: Why Study Computer Architecture?
Enable better systems: make computers faster, cheaper, smaller, more reliable, …
  By exploiting advances and changes in underlying technology/circuits
Enable new applications
  Life-like 3D visualization 20 years ago?
  Virtual reality?
Enable better solutions to problems
  Software innovation is built into trends and changes in computer architecture
    > 50% performance improvement per year has enabled
Understand why computers work the way they do

## Slide 41: Computer Architecture Today
Today is a very exciting time to study computer architecture
Industry is in a large paradigm shift (to multi-core)
Many problems motivating and caused by the shift
  Power/energy constraints
  Complexity of design  multi-core
  Technology scaling  new technologies
  Memory wall/gap
  Reliability wall/issues
  Programmability wall/problem

## Slide 42: What is A Computer?
Three key components
Computation
Communication
Storage (memory)

## Slide 43: Typical PC Architecture: northbridge or host bridge
front-side bus (FSB)
I/O controller hub

## Slide 44: (Typical PC Architecture) northbridge or host bridge
Graphics and Memory Controller Hub
(GMCH)
I/O Controller Hub (ICH)

## Slide 45: Intel 945 Express Chipset
Intel
Pentium D Processor
DDR2
DDR2
4 Serial ATA Ports
Integrated Matrix Storage Technology
6 PCI Slots
BIOS
Support
Support for Media Ext Card
Intel GMA 950 Graphics
PCI Express*
x16 Graphics
Intel HD Audio
8 high Speed USB Ports
6 PCI Express*
x1 slot
Intel Pro 100/1000 LAN
Intel Active
Mngement Tech.
82945
GMCH/MCH
North Bridge
82801 GR
ICH7 (io cont. hub sys7)
South Bridge

## Slide 46
What is A Computer?
Courtesy, Intel

## Slide 47: What is A Computer?
We will cover all three components
Memory
(program
and data)
I/O
Processing
control
(sequencing)
datapath

## Slide 48: The Von Neumann Model/Architecture
Also called stored program computer (instructions in memory). Two key properties:
Stored program
  Instructions stored in a linear memory array
  Memory is unified between instructions and data
    The interpretation of a stored value depends on the control signals
Sequential instruction processing
  One instruction processed (fetched, executed, and completed) at a time
  Program counter (instruction pointer) identifies the current instr.
  Program counter is advanced sequentially except for control transfer instructions
When is a value interpreted as an instruction?

## Slide 49: Dataflow Model (of a Computer)
Von Neumann model: An instruction is fetched and executed in control flow order
  As specified by the instruction pointer
  Sequential unless explicit control flow instruction
Dataflow model: An instruction is fetched and executed in data flow order
  i.e., when its operands are ready
  i.e., there is no instruction pointer
  Instruction ordering specified by data flow dependence
    Each instruction specifies “who” should receive the result
    An instruction can “fire” whenever all operands are received
  Potentially many instructions can execute at the same time
    Inherently more parallel

## Slide 50: Von Neumann vs Dataflow
Consider a von Neumann program
  What is the significance of the program order?
  What is the significance of the storage locations?
Which model is more natural to you as a programmer?
v <= a + b;
w <= b * 2;
x <= v - w
y <= v + w
z <= x * y
+
*2
-
+
*
a
b
z
Sequential
Dataflow

## Slide 51: ISA vs. Microarchitecture Level Tradeoff
A similar tradeoff (control vs. data-driven execution) can be made at the microarchitecture level
ISA: Specifies how the programmer sees instructions to be executed
  Programmer sees a sequential, control-flow execution order vs.
  Programmer sees a data-flow execution order
Microarchitecture: How the underlying implementation actually executes instructions
  Microarchitecture can execute instructions in any order as long as it obeys the semantics specified by the ISA when making the instruction results visible to software
    Programmer should see the order specified by the ISA

## Slide 52: ISA vs. Microarchitecture Level
ISA: Specifies how the programmer sees instructions to be executed
Microarchitecture: How the underlying implementation actually executes instructions
  Microarchitecture can execute instructions in any order as long as it obeys the semantics specified by the ISA when making the instruction results visible to software
    Programmer should see the order specified by the ISA

## Slide 53: The Von-Neumann Model
All major instruction set architectures today use this model
  x86, ARM, MIPS, SPARC, Alpha, POWER
Underneath (at the microarchitecture level), the execution model of almost all implementations (or, microarchitectures) is very different
  Pipelined instruction execution: Intel 80486 uarch
  Multiple instructions at a time: Intel Pentium uarch
  Out-of-order execution: Intel Pentium Pro uarch
  Separate instruction and data caches
But, what happens underneath that is not consistent with the von Neumann model is not exposed to software
  Difference between ISA and microarchitecture

## Slide 54: ISA vs. Microarchitecture
ISA
  Agreed upon interface between software and hardware
    SW/compiler assumes, HW promises
  What the software writer needs to know to write and debug system/user programs
Microarchitecture
  Specific implementation of an ISA
  Not visible to the software
Microprocessor
  ISA, uarch, circuits
  “Architecture” = ISA + microarchitecture
Microarchitecture
ISA
Program
Algorithm
Problem
Circuits
Electrons
Notes: ISA is the interface between hardware and software… It is a contract that the hardware promises to satisfy.
Builder/user interface

## Slide 55: CISC versus RISC
CISC | RISC
Emphasis on hardware | Emphasis on software
Includes multi-clock complex instructions | Single-clock, reduced instruction only
Memory-to-memory: "LOAD" and "STORE" incorporated in instructions | Register to register: "LOAD" and "STORE" are independent instructions
Small code sizes, high cycles per second | Low cycles per second, large code sizes
Transistors used for storing complex instructions | Spends more transistors on memory registers