## Slide 1: Peripheral Interface Device 8155 (I/O Interface & Timer)

## Slide 2: Outline
Review
  Programmable Interface device 8155
    Block diagram, Address Calculation diagram
    Interfacing LED using 8155
8155 Timer
  Modes of timer
  Square wave generation using 8155 interfaced timer
8155 Handshake & Interrupt mode
Interfacing A/D Converter using Handshake mode using 8155

## Slide 3: 8155 Block Diagram
RAM
Port
A
Port
B
Port
C
Timer
MSB LSB
PA0-PA7
PB0-PB7
PC0-PC5
Timer Out
Reset in
RD
WR
ALE
CE
IO/M
AD0-AD7
8155
Timer CLK

## Slide 4: Expanded Block Diagram
3 to 8 Decoder
CWR
Port
A
Port
B
Port
C
Timer
MSB LSB
Latch
Clock for timer
PA0-PA7
PB0-PB7
PC0-PC5
Timer Out
A0
A1
A2
ALE
AD0-AD7
A0-A7
D7-D0
0
1
2
3
4
5
CEb
A2 | A1 | A0 | Port (ALE high, AD0=A0)
0 | 0 | 0 | Command /Status Register
0 | 0 | 1 | PA
0 | 1 | 0 | PB
0 | 1 | 1 | PC
1 | 0 | 0 | Timer LSB
1 | 0 | 1 | Timer MSB

## Slide 5: Calculate Address of Port of 8155
3 to 8
Decoder
04
A13
A12
A11
A15
A14
A2
A1
A0
5V
3 to 8 Decoder
RAM
Control
CWR
Port
A
Port
B
Port
C
Timer
MSB LSB
Latch
Clock for timer
PA0-PA7
PB0-PB7
PC0-PC5
Timer Out
Reset in
RD
WR
A0
A1
A2
ALE
CE
IO/M
IO/M
AD0-AD7
A0-A7
D7-D0
20H
21H
22H
23H
24H
25H
CS
Instruction IN/OUT : Both Lower Address & Higher Address are same
D7/A15 | D6/A14 | D5/A13 | D4/D12 | D3/A11 | D2/A10 | D1/A9 | D0/A8
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0

## Slide 6: 8155 Block Diagram
3 to 8 Decoder
RAM
Control
CWR
Port
A
Port
B
Port
C
Timer
MSB LSB
Latch
Clock for timer
PA0-PA7
PB0-PB7
PC0-PC5
Timer Out
Reset in
RD
WR
A0
A1
A2
ALE
CE
IO/M
IO/M
AD0-AD7
A0-A7
D7-D0
8155
20H
21H
22H
23H
24H
25H

## Slide 7: Control word (command reg) format
D0, D1: mode for PA and PB, 0=IN, 1=OUT
D2, D3: mode for PC
D4, D5: interrupt EN for PA and PB, 0=disable 1=enable
D6, D7: Timer command:
  00: No effect
  01: Stop if running else no effect
  10: Stop after terminal count (TC) if running, else no effect
  11: Start if not running, reload at TC if running.
Port C bits
(D2, D3)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Timer Command |  | IEB | IEA | PC |  | PB | PA
ALT | D3 | D2 | PC5 | PC4 | PC3 | PC2 | PC1 | PC0
1 | 0 | 0 | IN | IN | IN | IN | IN | IN
2 | 0 | 1 | OUT | OUT | OUT | OUT | OUT | OUT
3 | 1 | 0 | OUT | OUT | OUT | STBA | BFA | INTRA
4 | 1 | 1 | STBB | BFB | INTRB | STBA | BFA | INTRA

## Slide 8: 8155 Decode Registers
Registers
A2 | A1 | A0 | Port (ALE high, AD0=A0)
0 | 0 | 0 | Command/Status Register
0 | 0 | 1 | PA
0 | 1 | 0 | PB
0 | 1 | 1 | PC
1 | 0 | 0 | Timer LSB
1 | 0 | 1 | Timer MSB

## Slide 9: Interfacing 7 Segment LEDs to output port using 8155
8155
PA7
PA6
PA5
PA4
PA3
PA2
PA1
PA0
PB7
PB6
PB5
PB4
PB3
PB2
PB1
PB0
AD7
to
AD0
IO/Mb
ALE
RDb
WRb
RESET OUT
IO/Mb
ALE
RDb
WRb
RESET OUT
7 Seg LED
Driver
7 Seg LED
Driver
7 Seg LED
Driver
7 Seg LED
Driver
3 to 8
Decoder
04
A13
A12
A11
A15
A14
A2
A1
A0
5V

## Slide 10: Interfacing LEDs Cntd..
Port Address
  Control Register=20H, Port A= 21H, Port B= 22H
Control word:
Program
  MVI A,03 ; initialize Port A &B for O/P
  OUT 20H
  MVI A, BYTE1 ; Display BYTE1 at port A
  OUT 21H
  MVI A, BYTE2 ; Display BYTE2 at port B
  OUT 22H
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
Timer |  | Not Applicable |  | Use for Port C |  | Port B Output | Port A Output

## Slide 11: 8155: Timers
M2, M1: mode bits:
  00: Single square wave of wavelength TC/2 (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  01: Square waves of wavelength TC (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  10: Single pulse on the TC'th clock pulse
  11: Single pulse on every TC'th clock pulse.
MSB |  |  |  |  |  |  | 
M2 | M1 | T13 | T12 | T11 | T10 | T9 | T8
LSB |  |  |  |  |  |  | 
T7 | T6 | T5 | T4 | T3 | T2 | T1 | T0

## Slide 12: 8155: Timer Modes Output
  00: Single square wave of wavelength TC/2 (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  01: Square waves of wavelength TC (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  10: Single pulse on the TC'th clock pulse
  11: Single pulse on every TC'th clock pulse.
CLK
WR
Mode 00
Mode 01
Mode 10
Mode 11
N/2
N/2
N/2
N/2
N/2
N/2
N
N
N

## Slide 13: Designing of Square Wave Generator Using 8155
Design a square wave with pulse width 100μS
Mode 1
Clock Frequency 3 MHZ
Timer count: Pulse Period/Clock period
= 200x10-6/330x10-9= 606
= 25E H
= 02 (MSB), 5E (LSB)

## Slide 14: Square Wave Generator Cntd..
Timer port address: LSB 24H & MSB 25H
Mode 1; M1=0, M2=1
  M1 M2 T13 T12 T11 T10 T8 T7
  0 1 0 0 0 0 1 0 == (42H)
Control word: (C0H)
Instructions to set counter & square wave generation
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
Timer Command |  | IEB | IEA | PC |  | PB | PA
1 |  | 0 | 0 | 0 0 |  | 0 | 0
MVI A , 5E ; LSB of count
OUT 24H ; Load LSB of timer Register
MVI A, 42H ; MSB count with Mode 1
MVI 25H ; Load MSB of timer Register
MVI A, C3H ; Load the control word for register
OUT 20H ; Trigger the counter by loading to Ctrl word to ctrl Reg

## Slide 15: Designing Interfacing Ckt Using 8155 to Read & Display from ADC to LEDs
Set up Port A in the handshake mode to read data from A/D Converter
Setup port B as output port to display data at seven segment LEDs
Use line PC3 from port C to initiate a conversion
Use the 8155 Timer to record conversation time

## Slide 16: Control, Status & Timer
Control word
Status word
Timer (with effecting other I/O assignment)
  Start timer
  Stop timer
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
Timer |  | NA (INTR not used) |  | Use for Port C |  | Port B OUT to LED | Port A IN from DAC
06H
CH=O/P
CL=Handshake Mode
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
No | X | X | X | X | X | BFa | X
USe | Timer | INTEb | BFb | INTRb | INTAa | BFa | INTRa
Read the Data
Mask with 02H
1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 0
C6H
46H

## Slide 17: Interface Diagram
8155
PA7
PA6
PA5
PA4
PA3
PA2
PA1
PA0
AD7
to
AD0
IO/Mb
ALE
RDb
WRb
RESET OUT
IO/Mb
ALE
RDb
WRb
RESET OUT
PB7
PB6
PB5
PB4
PB3
PB2
PB1
PB0
7 Seg LED
Driver
7 Seg LED
Driver
3 to 8
Decoder
04
A13
A12
A11
A15
A14
A2
A1
A0
ADC
5790
Analog
Input
Vi
DRb
B/Cb
PC2
PC3
Port CH = O/P
PC3 is used for Start Conversion
Port CL = HS mode
PC2 is STROBE

## Slide 18: Interfacing Program
MVI A,06H ;Control world for I/O port
OUT 20H ; Set up port as specified
MVI A,00H ; Load 0000H in Timer Reg
OUT 24H
OUT 25H
MVI A,08H ;Byte to set PC3=1
OUT 23H ;Send start pulse
MVI A,C6H ;Control word to start timer
MVI 20H ; Start timer
MVI A,00H ;Byte to set PC3=0
OUT 23H ;Start conversion
ST:IN 20H ; Read Status Register
ANI 02H ;Check Status of DRb
JZ ST ; If BFa=0 wait in
MVI A,46H ; Byte to stop Counter
OUT 20H ;Stop Counter
IN 21H ; Read A/D output
OUT 22H ;Display data at port B (LEDs)
INT 24H ; Read LSB of Timer
MOV L,A
INT 25H ; Read MSB of Timer
ANI 3FH ;Mask the mode Bit D6,D7
MOV H,A ; Save MSB timer count in H
LHLD RWM ; Store the count at
;Memory location RWM
HLT

## Slide 19: 8253/4 Programmable Interval Timer

## Slide 20: Hierarchy of I/O Control Devices
8155
I/O + Timer
8255
I/O
8253/54
Timer
2 Port (A,B),
No Bidirectional
HS mode (C)
4 mode timer
2 Port (A,B)
A is Bidirectional
HS mode (C)
Extra controls
6 mode timer
8259
Interrupt controller
8237
DMA controller
8251
Serial I/O USART controller

## Slide 21: Outline
Basic Difference of 8155 I/O timer Vs 8254
8254 Brief
Architecture of 8254
Control register
Status register
Modes of Counters with example
Read-Back modes

## Slide 22: 8254 Description
The 82C54 solves one of the most common problems in any microcomputer system, the generation of accurate time delays under software control.
Instead of setting up timing loops in software, the programmer configures the 82C54 to match his requirements and programs one of the counters for the desired delay. After the desired delay, the 82C54 will interrupt the CPU. Software overhead is minimal and variable length delays can easily be accommodated

## Slide 23: 8254 Description
Some of the other counter/timer functions common to microcomputers which can be implemented with the 82C54 are:
  Real time clock
  Event counter
  Digital one-shot
  Programmable rate generator
  Square wave generator
  Binary rate multiplier
  Complex waveform generator
  Complex motor controller

## Slide 24: 8254 Chip
Main function:
  Dividing clock frequency
Three independent 16-bit counters
Models
  8253: 2 MHz
  8254: 8 MHz
  8254-2: 10 MHz

## Slide 25: 8155: Timer Modes Output
  00: Single square wave of wavelength TC/2 (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  01: Square waves of wavelength TC (TC/2,TC/2 if TC even; [TC+1/2],[TC-1/2] if TC odd)
  10: Single pulse on the TC'th clock pulse
  11: Single pulse on every TC'th clock pulse.
CLK
WR
Mode 00
Mode 01
Mode 10
Mode 11
N/2
N/2
N/2
N/2
N/2
N/2
N
N
N

## Slide 26: 8254: Brief
Three independent 16-bit programmable counters (timers).
It generates accurate time delays and can be used for
  Real time clock, an event Ctr, a digital one shot, a square wave gen, complex wave gen.
Programmable and work DC to 8 MHz
5 different modes of operation

## Slide 27: The 8254 PIT
The 8254 Programmable Interval-timer is used by the PC system for (1) generating timer-tick interrupts (rate is 18.2 per sec), (2) performing dynamic memory-refresh (reads ram once every 15 microseconds), and (3) generates ‘beeps’ of PC speaker
When the speaker-function isn’t needed, the 8254 is available for other purposes

## Slide 28: 8254 Block Diagram
Data
Bus
Buffer
Read/
Write
Logic
Counter
0
CLK 0
GATE 0
OUT 0
Internal
Bus
Control Word
Register
Counter
1
CLK 1
GATE 1
OUT 1
Counter
2
CLK 2
GATE 2
OUT 2
D0-D7
RDb
WRb
A0
A1
CSb

## Slide 29: Control Logic
RDb, WRb, CSb
A0, A1: Selection of Counter and Control Register
Suppose Address is (80H,81H,82H,83H) with interfacing Circuit
A1 | A0 | Selection
0 | 0 | Counter 0
0 | 1 | Counter 1
1 | 0 | Counter 2
1 | 1 | Control Register

## Slide 30: Control Register
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SC1 | SC2 | RW1 | RW0 | M2 | M1 | M0 | BCD
Select Counter 00: Counter 0 01: Counter 1 10: Counter 2 11: Read-Back Command |  | Read Write 00: Counter latch Command 01:RW LSByte only 10: RW MSByte only 11:RW LSByte first then Msbyte |  | 000 : Mode 0 001 :Mode 1 X10 :Mode 2 X11 :Mode 3 100 :Mode 4 101 : Mode 5 |  |  | 0/1 = Binary / BCD Mode

## Slide 31: Programming Counters
Each counter may be programmed with a count of 1 to FFFFH.
  Minimum count is 1 all modes except 2 and 3 with minimum count of 2.
Each counter has a program control word used to select the way the counter operates.
  If two bytes are programmed, then the first byte (LSB) stops the count, and the second byte (MSB) starts the counter with the new count.

## Slide 32: Modes of 8254 Counter
Mode 0 : Interrupt on Terminal count
Mode 1 : Hardware Retriggerable One Shot
Mode 2 : Rate Generator
Mode 3 : Square wave generator
Mode 4 : Software Triggered Strobe
Mode 5 : Hardware Triggered Strobe

## Slide 33: Mode 0: Interrupt on Terminal Count
The output becomes a logic 0 when the control word is written and remains there until N plus the number of programmed counts.
CLK
OUT
Count of 7 loaded

## Slide 34: Mode 1: Hardware Retriggerable One Shot
The G input triggers the counter to output a 0 pulse for `count' clocks.
Counter reloaded if G is pulsed again.
CLK
GATE
OUT
Triggered with count of 5

## Slide 35: Mode 2: Rate Generator
Counter generates a series of pulses 1 clock pulse wide.
The separation between pulses is determined by the count.
The cycle is repeated until reprogrammed or G pin set to 0.
CLK
OUT
Count of 5 loaded

## Slide 36: Write instruction to generate pulse every 50mcroS from Ctr0
Control word = 14H
  D7D6=00 Select ctr 0
  D5D4=01 load 8 bit count
  D3D2D1=010 mode 2
  D0=0 Binary
Count = 50x10-6/0.5x10-6=64H
PULSE: MVI A 14H ; Control word
OUT CTRAdd 83H
MVI A,64H ;Count value
OUT 80H ; load counter 0 with low
order byte
HALT

## Slide 37: Mode 3: Square wave generator
Generates a continuous square-wave with G set to 1.
If count is even, 50% duty cycle otherwise OUT is high 1 cycle longer
CLK
OUT
Count of 6 loaded

## Slide 38: Write instruction for 1KhZ square wave at Ctr 1
Control word = 76H
Count= 1x10-3/0.5x10-6=2000=07D0H
Instructions
  MVI A,76H ; load Control word for Ctr 1 mode 3
  OUT 83H ; write to Ctrl reg
  MVI A, D0H; lower order byte cnt
  OUT 81H
  MVI A,07H ; higher order byte
  OUT 81H
  HLT
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SC1 | SC2 | RW1 | RW0 | M2 | M1 | M0 | BCD
01 |  | Load 16 bit (11) |  | 011 (mode 3) |  |  | 0

## Slide 39: Mode 4: Software Triggered Strobe
Software triggered one-shot (G must be 1).
OUT goes initially High, it goes low for one clock at the end of count
The count must be reloaded for subsequent output
CLK
OUT
Triggered with count of 8

## Slide 40: Mode 5: Hardware Triggered Strobe
Hardware triggered is one-shot
It is triggered by rising edge at the Gate
Initially the OUT is low and Gate triggered from low to high the count begins
OUT goes low for one clock period
H/W trigger with count of 8
CLK
OUT

## Slide 41: Example

## Slide 42: Example 2

## Slide 43: 8253 Decoding in PC

## Slide 44: PC Board

## Slide 45: Write a pgm to generate an interrupt every 1 Second
Assume Clock Freq=2MhZ
Count is too large
Counter 1 load with 50,000 to generate 25ms
  CNTLOAD=50,00010=C350H
Counter 2 load with 40 to generate 25msX40=-1S pulse (CNTLOAD=4010=28H)
Counter1 input is to counter 2
Both Counter 1 & Counter 2 in Mode 2

## Slide 46: Instruction to set up 1s interrupt
MVI A , 74H ; Mode for 1st CTR
OUT 83H ;Write in control register
MVI A,94H ; Mode for 2nd CTR
OUT 83H ; Write to control register
MVI A,50 ; low byte of CTR1=C350
OUT 81H ; load to CTR1 low byte
MVI A,C3 ; high byte of CTR1=C350
OUT 81H ; load to CTR1 high byte
MVI A,28H ; Count for Counter 2
OUT 82H ; Load Counter 2
RET

## Slide 47: Gate Setting of Counter
Modes | Low or Going Low | Rising | High
Mode 0 | Disable Counting | - | Enable Counting
Mode 1 | ----- | 1. Initiate Counting 2. Reset O/P after next Clock | ---
 | Disable counting Set O/P immediately high | Reloads Counter Initiate Counting | Enable Counting
 | Disable counting Set O/P immediately high | Initiates Counting | Enable Counting
 | Disable Counting |  | Enable Counting
 |  | Initiates Counting | 

## Slide 48: Read-Back Command
This allow user to read the count and status of the counter
Command Written in control register and count of the specified counter can be latched
Control word 11 01 011 0 (D6H) in control word will latch the count of CNT0 & CNT1
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SC1 | SC2 | COUNTb | STATUSb | CNT2 | CNT1 | CNT0 | 0
11: Read-Back Command |  | If (D5=0) count is lateched |  | D3=1 select counter 2 D2=1 select counter 1 D1=1 select counter 0 |  |  | 

## Slide 49: Read-Back Command
Status can be read if STATUSb bit D4 =0
D7=1 : Outpin is 1, 0 Outpin is 0
D6=1: Null count, D6: 0= Count available for reading
D5-D0:Counter Programmed mode
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
OUTPUT | NULL COUNT | RW1 | RW0 | M2 | M1 | M0 | BCD

## Slide 50: Control word
Counter 1 (74H)
Counter 2 (94H)
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SC1 | SC2 | RW1 | RW0 | M2 | M1 | M0 | BCD
01 |  | Load 16 bit (11) |  | 010 (mode 2) |  |  | 0
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
SC1 | SC2 | RW1 | RW0 | M2 | M1 | M0 | BCD
10 |  | Load 8 bit (01) |  | 010 (mode 2) |  |  | 0

## Slide 51: Outline
Peripheral communications
DAC
  Properties
  Generic Model
  Interfacing
ADC
  Properties
  Generic Model
  Interfacing
Display

## Slide 52: Digital to Analog Converter
Used for play sound in speaker
Used by AC97 (Audio codec)
MP3 Sound store digital format in HDD
  Slow as compared to processor/MPU
  Parameters
    Resolution (8 bit/16 bit)
    Settling time (1micro sec)

## Slide 53: D/A converter
FullScaleOutput=(FullScaleValue – 1LSBValue)
1MSB Value=1/2 * FSV
Digital
to
Analog
Converter
D0
D1
D2
Analog Output
Vo
Digital Inputs
Analog output
000
001
011
010
100
101
111
110
LSB
FS
0
1
2
3
4
5
6
7

## Slide 54: Circuit Realization
4K
2.5K
5K
10K
20K
D3=8
D2=4
D1=2
D0=1
Vout
Vo= Vref/R * ( A1/2+ A2/4+…An/2n)
Vo is proportional to values of Data Bits Value

## Slide 55: Practical DAC : R-2R ladder network
Resistive Ladder Network
Require two type Resistor
But small value
  5K and 10K
2R||2R=R
R+R=2R
R
2R
2R
2R
2R
R
Vout
R
R
+
Resistor
R
E
G
I
S
T
E
R

## Slide 56: Output Glitches
Glitches cause waveform distortion, spurs and elevated noise floors
High-speed DAC output is often followed by a de-glitching SHA (Hold Buffer)
Cause: Signal and clock skew in circuits
Especially severe at MSB transition where all bits are switching –
0111…111 →
1000…000

## Slide 57: Performance of DAC
Resolution
Reference Voltages
Settling Time
Linearity
Speed
Errors

## Slide 58: Resolution
Amount of variance in output voltage for every change of the LSB in the digital input.
How closely can we approximate the desired output signal(Higher Res. = finer detail=smaller Voltage divisions)
A common DAC has a 8 - 12 bit Resolution
N = Number of bits

## Slide 59
Better Resolution(3 bit)
Poor Resolution(1 bit)
Vout
Desired Analog signal
Approximate output
2 Volt. Levels
Digital Input
0
0
1
Digital Input
Vout
Desired Analog signal
Approximate output
8 Volt. Levels
000
001
010
011
100
101
110
111
110
101
100
011
010
001
000
Resolution

## Slide 60: Reference Voltage
A specified voltage used to determine how each digital input will be assigned to each voltage division.
Types:
  Non-multiplier: internal, fixed, and defined by manufacturer
  Multiplier: external, variable, user specified

## Slide 61: Settling Time
Settling Time: The time required for the input signal voltage to settle to the expected output voltage(within +/- VLSB).
Any change in the input state will not be reflected in the output state immediately. There is a time lag, between the two events.

## Slide 62: Settling Time
Analog Output Voltage
Expected Voltage
+VLSB
-VLSB
Settling time
Time

## Slide 63: Linearity
Linearity(Ideal Case)
Digital Input
Perfect Agreement
Desired/Approximate Output
Analog Output Voltage
NON-Linearity(Real World)
Analog Output Voltage
Digital Input
Desired Output
Miss-alignment
Approximate output

## Slide 64: Errors Gain
Gain Error: Difference in slope of the ideal curve and the actual DAC output
High Gain Error: Actual slope greater than ideal
Low Gain Error: Actual slope less than ideal
Digital Input
Desired/Ideal Output
Analog Output Voltage
Low Gain
High Gain

## Slide 65: Speed
Rate of conversion of a single digital input to its analog equivalent
Conversion Rate
  Depends on clock speed of input signal
  Depends on settling time of converter

## Slide 66: Generic Used: Audio player
Used when a continuous analog signal is required.
Signal from DAC can be smoothed by a Low pass filter
0 bit
nth bit
n bit DAC
011010010101010100101
101010101011111100101
000010101010111110011
010101010101010101010
111010101011110011000
100101010101010001111
Digital Input
Filter
Piece-wise Continuous Output
Analog Continuous Output

## Slide 67: Interfacing 8-bitDAC with 8085
Design an output port with Address FFH to interface 1408 DAC
Write a program to generate a continuous RAMP waveform
Time
Output

## Slide 68: Interfacing Diagram
8085
MPU
A15
A0
D0
D7
Address Bus (16bit)
Data Bus (8bit)
A7
A6
A5
A4
A3
A2
A1
A0
74LS373
Latches
1408
LE
D7
D6
D5
D4
D3
D2
D1
D0

## Slide 69: Program to generate continuous RAMP waveform
  MVI A, 00H ; Load Acc with first I/P
  DTOA: OUT FFH ; Output to DAC
  MVI B, COUNT ; Setup Reg. for Delay
  DCR B
  JNZ DELAY
  INR A ; Next Input
  JMP DTOA ; Go back to Output
Slope of RAMP can be varied by changing Delay

## Slide 70: Analog to Digital Conversion
ADC are slower then DAC
Interfaced using Status Check
Analog to Analog
Converter
D0
D1
D2
Analog Input
Vi
Analog Input
Digital output
LSB
000
001
010
011
100
101
110
111
0 1 2 3 4 5 6 7

## Slide 71: Sampling Concepts
Sampling
Fourier Transform

## Slide 72: Interpolation
The process of reconstructing a signal from its values at discrete instants of time
  Zero order hold or One Point
  Linear or Two Point
  Band limited or Low pass Filtering

## Slide 73: A/D Conversion Techniques
Counter or Tracking ADC
Successive Approximation ADC
  Most Commonly Used
Parallel or Flash ADC
  Fast Conversion

## Slide 74: Counter Type ADC
Block diagram
Waveform
Operation
  Reset and Start Counter
  DAC convert Digital output of Counter to Analog signal
  Compare Analog input and Output of DAC
    Vi < VDAC
      Continue counting
    Vi = VDAC
      Stop counting
  Digital Output = Output of Counter
Disadvantage
  Conversion time is varied
    2n Clock Period for Full Scale input
Clock
Control
Logic
Counter
DAC
Vi

## Slide 75: Successive Approximation ADC
Most Commonly used in medium to high speed Converters
Based on approximating the input signal with binary code and then successively revising this approximation until best approximation is achieved
SAR(Successive Approximation Register) holds the current binary value
Block Diagram

## Slide 76: Successive Approximation ADC
Circuit waveform
Logic Flow
Conversion Time
  n clock for n-bit ADC
  Fixed conversion time
Serial Output is easily generated
  Bit decision are made in serial order

## Slide 77: Parallel or Flash ADC
Very High speed conversion
  Up to 100MHz for 8 bit resolution
  Video, Radar, Digital Oscilloscope
Single Step Conversion
  2n –1 comparator
  Precision Resistive Network
  Encoder
Resolution is limited
  Large number of comparator in IC

## Slide 78: Generic ADC
A/D
Converter
Digital O/P
Vinput
Start
Ready
START
RD

## Slide 79: Interface ADC using Status Check
A/D
Converter
Digital O/P
Vinput
Start
Ready
START
RD
Tri-State
Buffer
8085
MPU
A15
A0
D0
D7
Address Bus (16bit)
Data Bus (8bit)
A6
A5
A4
A3
IO/W
74
LS
138
E1
E2
E3
A7
IO/R
o2
o1
o0
82H
81H
80H

## Slide 80: Program to Interface ADC
OUT 82H ; Start Conversion
TEST: IN 80H ;Read DR Status
RAR ; Rotate Do to carry
JC TEST ; if Do==1 conv. done
IN 81H ; Read the output
RET ; Return

## Slide 81: Interrupt Controller (8259)

## Slide 82: A Taxonomy of Interrupts

## Slide 83: The Purpose of Interrupts
Interrupts are useful when interfacing I/O devices at relatively low data transfer rates, such as keyboard inputs
Interrupt processing allows the processor to execute other software while the keyboard operator is thinking about what to type next.
Notes:   a time line shows typing on a keyboard, a printer removing data from memory, and a program executing

## Slide 84: Interrupt Vector Table
03FF
03FE
03FD
03FC
0007
0006
0005
0004
0003
0002
0001
0000
int type 255
Int type 0
Int type 1
Memory in Hex
IP High Byte
IP Low byte
IP High Byte
CS Low Byte
IP High Byte
IP Low byte
IP High Byte
CS Low Byte
IP High Byte
IP Low byte
IP High Byte
CS Low Byte

## Slide 85: Figure 12–2 (a) The interrupt vector table for the microprocessor and (b) the contents of an interrupt vector.
  the first five interrupt vectors are identical in all Intel processors
  Intel reserves the first 32 interrupt vectors
  the last 224 vectors are user-available
  each is four bytes long in real mode and contains the starting address of the interrupt service procedure.
  the first two bytes contain the offset address
  the last two contain the segment address

## Slide 86: Example
Question: A particular interrupt has a type number n=41H. If the corresponding ISR begins at address
FE00:0500H, determine the locations in the vector table to store this address.
Solution: The vector address is calculated by multiplying 41H by four.
00104:00; 00105:50; 00106:00; 00107:FE;

## Slide 87: Interrupt Vector Table (x86)
Using the Interrupt Vector Table shown below, determine the address of the ISR of a device with interrupt vector 42H.
Answer: Address in table = 4 X 42H = 108H
(Multiply by 4 since each entry is 4 bytes)
Offset Low = [108] = 2A, Offset High = [109] = 33
Segment Low = [10A] = 3C, Segment High = [10B] = 4A
Address = 4A3C:332A = 4A3C0 + 332A = 4D6EAH

## Slide 88: Interrupt Processing
When interrupt occurs, normal processing is suspended while a special Interrupt Service Routine (ISR) is executed. Normal processing resumes when this routine is completed.

## Slide 89: Interrupt Processing

## Slide 90: A simple method for generating interrupt vector type number FFH in response to INTR

## Slide 91: Using a Three-State Buffer for INTA
Interrupt vector type number 80H is applied to the data bus (D0–D7) in response to an INTR.
In response to INTR, the processor outputs the INTA to enable a 74ALS244 three-state octal buffer.
The octal buffer applies the interrupt vector type number to the data bus in response.
The vector type number is easily changed with DIP switches shown in this illustration.

## Slide 92: A circuit that applies any interrupt vector type number in response to INTA. Here the circuit is applying type number 80H.

## Slide 93: 82C55 interfaced to a keyboard from the microprocessor system using interrupt vector 40H.
Every time a key is typed, 82C55 requests a type 40H interrupt through the INTR pin

## Slide 94: EXPANDING THE INTERRUPT STRUCTURE
The common methods of expanding the interrupt structure of the processor.
  Using the 74ALS244 to Expand Interrupts
  expand the INTR input so it accepts seven interrupt inputs.
The only hardware change is the addition of an eight-input NAND gate, which provides the INTR signal to the microprocessor when any of the IR inputs becomes active

## Slide 95: Expanding the INTR input from one to seven interrupt request lines

## Slide 96: Operation
If any of the IR inputs becomes logic 0, the output of the NAND gate goes to logic 1 and requests an interrupt through the INTR input.
The interrupt vector that is fetched during the pulse depends on which interrupt request line becomes active.
  the interrupt vectors used by a single interrupt request input
What happens if two or more interrupt requests are active, a new interrupt vector is generated?
IR6 | IR5 | IR4 | IR3 | IR2 | IR1 | IR0 | Vector
1 | 1 | 1 | 1 | 1 | 1 | 0 | FE h
1 | 1 | 1 | 1 | 1 | 0 | 1 | FD h
1 | 1 | 1 | 1 | 0 | 1 | 1 | FB h
1 | 1 | 1 | 0 | 1 | 1 | 1 | F7 h
1 | 1 | 0 | 1 | 1 | 1 | 1 | EF h
1 | 0 | 1 | 1 | 1 | 1 | 1 | DF h
0 | 1 | 1 | 1 | 1 | 1 | 1 | BF h
Notes: The vector is address generated by the address group IR6_bar – IR0_bar

## Slide 97: Block Diagram of 8259
8259A
Programmable
Interrupt
Controller
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7
8 bit
Data Bus
RDb
WRb
CSb
A0
INT
INTAb
SPb/ENb

## Slide 98: Block Diagram Architecture of 8259
Control Logic
Interrupt Service
Register
Priority Resolver
Interrupt Request
Register
IRQ0
IRQ1
IRQ2
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7
Interrupt Mask Register
Internal Bus
INTAb
INT

## Slide 99: Connecting a single 8259A controller

## Slide 100: Three internal registers
IRR
IMR
ISR
8259A
IRR = Interrupt Request Register
IMR = Interrupt Mask Register
ISR = In-Service Register
output-signal
input-signals

## Slide 101
The processor responds to INTR by pulsing INTA output in anticipation of receiving an interrupt vector type number on data bus connections D7–D0.
Two INTA pulses generated by the system insert the vector type number on the data bus.

## Slide 102
INTR:
  The INTR input must be externally decoded to select a vector.
  Intel has reserved interrupts 00H - 1FH for internal and future expansion.
  Any interrupt vector can be chosen for the INTR pin, but we usually use an interrupt type number between 20H and FFH.
INTA:
  it is an output used in response to INTR input to apply a vector type number to the data bus connections D7–D0

## Slide 103: Adding Interrupts to the Hardware
Programmable Interrupt Controller: The 8259A chip
  Each Chip supports eight interrupt request (IRQ) lines
  Asserts INTR to CPU, responds to resulting INTA# with an 8-bit interrupt vector (“0xdd”) on the data bus
Industry Standard Architecture (ISA) Bus
  Priority: highest to lowest order is IRQ0-1, IRQ8-15, IRQ3-7
Master
8259
IRQ0
IRQ1
IRQ3
IRQ4
IRQ5
IRQ6
IRQ7
Slave
8259
IRQ8
IRQ9
IRQ10
IRQ11
IRQ12
IRQ13
IRQ14
IRQ15
To CPU

## Slide 104: Priority Modes
Fully Nested Modes
  IR are arranged in IR0-IR7 and Any IR can be assigned Highest or lowest priority IR4=0 (high), IR3=7 (low)
Automatics Rotation Mode
  A device after being served, receive the lowest priority with value 7 0123456712345670 23456701
Specific Rotation Mode
  User can select any IR for lowest priority 0673451267345120 73451206
EOI: End of interrupt
  Specific EOI Command
  Automatic EOI: no command necessary
  Non-Specific EOI: it resets the ISR bit

## Slide 105: Control Word (initialization)
CS | A0 | Initialization
0 | 0 | ICW1
0 | 1 | ICW2,ICW3,ICW4
1 | X | Not Address

## Slide 106: ICW1 & ICW2
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 0 | 0 | 1 | LTIM | 0 | SGNL | IC4
 | 0 for x86 |  |  |  | 1 for Level Trigger 0 for Edge Trigger |  | 1=single 0=Cascade | 
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | T7 | T6 | T5 | T4 | T3 | T2 | T1 | T0
 | T7=T0 is the assign to IR0, Vector address for ISR |  |  |  |  |  |  | 

## Slide 107: Masking and Prioritization
OCW (operation command word)
CS | A0 | Operation Command Word
0 | 0 | OCW1
0 | 1 | OCW2,OCW3,OCW4
1 | X | Not Address

## Slide 108: Programming OCWs: OCW1, OCW2
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | M7 | M6 | M5 | M4 | M3 | M2 | M1 | M0
 | Interrupt Masks: 1= Mask Set, 0 =Mask reset |  |  |  |  |  |  | 
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | R | SL | EOI | 0 | 0 | L2 | L1 | L0
 | Roteate | Specific | EOI |  |  | IR Level to be acted Upon (0-7) |  | 

## Slide 109: Example: Setting of control word
8259
IR0
IR1
IR2
IR6
Emergency
A/D converter
Keyboard
Printer
3-to-8
Decoder
CSb
A0
E1b E2b E3
A2
A1
A0
A3
A2
A1
A7
A6
A5
A0
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | M7=0 | M6=1 | M5=1 | M4=1 | M3=1 | M2=1 | M1=1 | M0=1
 | Interrupt Masks: 1= Mask Set, 0 =Mask reset |  |  |  |  |  |  | 
OCW1=7F
ADDRESS= 80H, 81H
04

## Slide 110: Initialization words (ICW1 & ICW2)
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
 | A7, A6,A5 Lower address bit of Vector Address |  |  |  | 0 for Edge Trigger | Call Address interval =4 | 1=single 0=Cascade | 
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | T7 | T6 | T5 | T4 | T3 | T2 | T1 | T0
 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
 | T7=T0 is the assign to IR0, Vector address for ISR Lower Byte of call address |  |  |  |  |  |  | 
76H
20H
Vector Address 2060, 2064…. | 0100 0000 | 0 1 1 | 00000

## Slide 111: Program to initialize
DI
MVI A, 76H ;move ICW1 byte to ACC
OUT 80H ; initialize 8259A ICW1
MVI A, 20H ; mov ICW2 byte to ACC
OUT 81H ; Initialize 8259A ICW2
MVI A, 7FH ; Put the OCW1
OUT 80H

## Slide 112: Nested mode
By Default 8259 work in Nested modes
  Unless we put a different OCW
Suppose IR2 has highest priority and IR6
IR6 is being serviced
IR2 can be nested iff IR6 IRS issue an EI command
Address of IR2=2068, IR2=2074

## Slide 113: Nested Interrupt process
EI
EI
RET
EI
DI
EOI
EI
RET
Interrupt at IR6
Interrupt at IR2
It wait up to EI instruction
IR2 has highest priority
IR6 has lower priority

## Slide 114: Maskable Interrupt
Those interrupt service can be temporarily disable to let the higher priority interrupt ISR to be executed without interruption
I want IR7 to be Non Maskable
AD0 | D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
1 | M7=0 | M6=1 | M5=1 | M4=1 | M3=1 | M2=1 | M1=1 | M0=1
 | Interrupt Masks: 1= Mask Set, 0 =Mask reset |  |  |  |  |  |  | 
OCW1=7F

## Slide 115
DMA Controller (8237 )

## Slide 116: Outline
DMA controller
DMA Architecture
  Registers
Introduction to Programming DMA
  How to configure

## Slide 117: Data Transfer DMA mode
Memory
CPU
DMA
Controller
CPU
I/O
System Bus
Memory
I/O
System Bus

## Slide 118: Data Transfer : DMA
Problems with programmed I/O
  Processor wastes time polling
  Lets take example of Key board
    Waiting for a key to be pressed,
    Waiting for it to be released
    May not satisfy timing constraints associated with some devices : Disk read or write
DMA
  Frees the processor of the data transfer responsibility

## Slide 119: Basic DMA Definitions
Direct memory accesses normally occur between an I/O device and memory without the use of the microprocessor.
  a DMA read transfers data from the memory to the I/O device
  A DMA write transfers data from an I/O device to memory
Memory & I/O are controlled simultaneously.
  which is why the system contains separate memory and I/O control signals

## Slide 120
A DMA read causes the MRDC and IOWC signals to activate simultaneously.
  transferring data from memory to the I/O device
A DMA write causes the MWTC and IORC signals to both activate.
The DMA controller provides memory with its address, and controller signal (DACK) selects the I/O device during the transfer.
8086/8088 require a controller or circuit (next slide) for control bus signal generation.

## Slide 121: A circuit that generates system control signals in a DMA environment.

## Slide 122
Data transfer speed is determined by speed of the memory device or a DMA controller.
  if memory speed is 50 ns, DMA transfers occur at rates up to 1/50 ns or 20 M bytes per second
  if the DMA controller functions at a maximum rate of 15 MHz with 50 ns memory, maximum transfer rate is 15 MHz because the DMA controller is slower than the memory
In many cases, the DMA controller slows the speed of the system when transfers occur.
Notes: The switch to serial data transfers in modern systems has made DMA is less important.
The serial PCI Express bus transfers data at rates exceeding DMA transfers.
The SATA (serial ATA) interface for disk drives uses serial transfers at the rate of 300 Mbps
  and has replaced DMA transfers for hard disks
Serial transfers on main-boards between components using can approach 20 Gbps for the PCI Express connection.

## Slide 123: DMA Controller
Interrupt
Controller
I/O Controller
DMA
Controller
IREQ
DREQ
DACK
IORDb
IOWRb
EOPb
MEMRDb
MEMWRb
INTR
HOLD
HOLDA
Data Bus
Address Bus
CPU
Memory

## Slide 124: DMA Controller
DMA is implemented using a DMA controller
DMA controller
  Acts as slave to processor
  Receives instructions from processor
  Example:
    Reading from an I/O device
    Processor gives details to the DMA controller
      I/O device number
      Main memory buffer address
      Number of bytes to transfer
      Direction of transfer (memory  I/O device, or vice versa)

## Slide 125: DMA: HOLD and HOLDA
HOLD: DMA to CPU
  DMA Send HOLD High to CPU
    I (DMA) want BUS Cycles
HOLDA
  CPU send HOLDA
    BUS is granted to DMA to do the transfer
    DMA became Slave to Master mode
HOLD Low to CPU
  I (DMA) finished the transfer
Cycle Stealing if One BUS
Other wise Separate process independent of processing

## Slide 126: Steps in a DMA operation
Processor initiates the DMA controller
  Gives device number, memory buffer pointer, … Called channel initialization
  Once initialized, it is ready for data transfer
    When ready, I/O device informs the DMA controller
      DMA controller starts the data transfer process
        Obtains bus by going through bus arbitration
        Places memory address and appropriate control signals
        Completes transfer and releases the bus
        Updates memory address and count value
        If more to read, loops back to repeat the process
Notify the processor when done

## Slide 127: 8237 DMA Controller
Enable/Disable control of Individual DMA Req
Four Independent DMA Channel
Independent Auto initialization for all channel
Memory to Memory transfer
Memory Block initialization
Address Increment and Decrement
Cascade (Directly expandable to any #CHN)
End of Process input for terminating transfers
Software DMA requests

## Slide 128: The 8237A programmable DMA controller. (a) Block diagram and (b) pin-out. (Courtesy of Intel Corporation.)

## Slide 129: 8237 DMA Controller
DMA Request 0
DMA Request 1
DMA Request 2
DMA Request 3
Hold Ack
Clock
Reset
Ready
Chip Select
Address Strobe
Hold request
DMA ack0
DMA ack1
DMA ack2
DMA ack3
IO Read
I/O Write
Memory Read
Memory Write
End of Process
To data Bus
To Address Bus
DREQ0
DREQ1
DREQ2
DREQ3
HLDA
CLK
RESET
READY
CSb
DB0-DB7
A0-A3
A4-A7
ADSTB
HOLD
DACK0
DACK1
DACK2
DACK3
IORDb
IOWRb
MemRDb
MemWRb
EOPb
Notes: Address strobe functions as ALE, except it is used by the DMA controller to latch address bits A15–A8 during the DMA transfer.

## Slide 130: DMA Controller with Internal Registers
Reg Addr
Meaning
00
CH0 memory Add reg
01
CH0 Count reg
02
CH1 memory Add reg
03
CH1 Count reg
04
CH2 memory Add reg
05
CH2 Count reg
06
CH3 memory Add reg
07
CH3 Count reg
08
status/Commnd reg
09
request reg
10
Single mask reg
11
mode reg
12
Clear byte ptr F/F
13
Master Clear/Temp
14
Clear Mask Reg
15
all Mask clear bits
DB7-DB0
3 to 8
Decoder
00
CSb
DREQ0
DREQ1
DREQ2
DREQ3
DACK0
DACK1
DACK2
DACK3
EOP
ADSTB
AEN
MEMRb
MEMWb
IORb
IOWb
READY
RESET
CLK
HRQ
HLDA
IO/Mb
A7
A6
A5
A4
A3
A2
A1
A0
A4-A7

## Slide 131: Figure 13–10 8237A-5 command and control port assignments. (Courtesy of Intel Corporation.)

## Slide 132: DMA interface to I/O Device
MP
Latch/Transceiver
Control Logic
8237A
Latch/Logic
Memory
I/O
0
I/O
3
Address Bus
Data bus
Control Bus
DACK0
DREQ0
DACK3
DREQ3
HLD
HLDA
HLD
HLDA
A8-A15
AD0-AD7
ALE
RDb
WRb
IOMb
AEN
ADSTB
MRW
IRW

## Slide 133: 8237 DMA channels
8237 supports four DMA channels
Handshake of I/O
  DREQ3-DREQ0 (DMA Request)
  DACK3-DACK0 (DMA Acknowledge)
AEN & ADSTB : Address Enable & Add Strobe
A3-A0 and A4-A7: Address line
HRQ and HLDA: Hold Request and Hold Ack
  Request hold BUS
Notes: The address enable (AEN) output of 8237 controls the output pins of the latches and outputs of the 74LS257 (E).
  during normal operation (AEN=0), latches A & C and the multiplexer (E) provide address bus bits A19–A16 and A7–A0

## Slide 134: Registers of 8237A
Command registers
Mode register
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0/1 | 0/1 | 0/1 | 0/1 | 0/1 | 0/1 | 0/1 | 0/1
DACK Sense Active Low/High | DREQ Sense Active Low/High | Late/Extended Write Selection | Fixed/ Rotating Priority | Normal/ Compressed Timing | Enable/Disable Controller | Dis/En CH0 Addres Hold | Dis/En Mem-mem Transfer
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
 |  | 0/1 | 0/1 |  |  |  | 
00=Demand Mode 01=Single Mode 10=Block Mode 11=Cascade mode |  | INC/DEC Address | Dis/Ena Auto Initialisation | 00=verify transfer 01=Write Transfer 10=Read transfer 11=Illegal |  | Channel Select 00=CH0, 01=CH1 10=CH2, 11=CH3 | 

## Slide 135: DMA Registers
Request register
Mask register: Used to disable a specific channel
Status register
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
XXXXX Don’t Care |  |  |  |  | Reset/Set REQ bit | 00-11 Channel Select 00=CH0, 01=CH1, 10=CH2, 11 CH3 | 
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
XXXX Don’t Care |  |  |  | 0/1 | 0/1 | 0/1 | 0/1
 |  |  |  | Clear/Set CH3 Mask Bit | Clear/Set CH2 Mask Bit | Clear/Set CH1 Mask Bit | Clear/Set CH0 Mask Bit
D7 | D6 | D5 | D4 | D3 | D2 | D1 | D0
0/1, CH3 | 0/1,CH2 | 0/1, CH1 | 0/1, CH0 | 0/1, CH3 | 0/1, CH2 | 0/1, CH1 | 0/1, CH0
CH# Request |  |  |  | CH# Has reached TC |  |  | 

## Slide 136: Registers
Temporary register
  Used for memory-to-memory transfers
Current address register
  One 16-bit register for each channel
  Holds address for the current DMA transfer
Current word register
  Keeps the byte count
  Generates terminal count (TC) signal when the count goes from zero to FFFFH

## Slide 137: Type of Data Transfer using 8237 DMA
Single transfer
  Useful for slow devices,
Block transfer mode
  Transfers data until TC is generated or external EOPb signal is received
Demand transfer mode
  Similar to the block transfer mode
  In addition to TC and EOP, transfer can be terminated by deactivating DREQ signal
Cascade mode
  Useful to expand the number channels beyond four

## Slide 138
Four steps are required to program the 8237:
  (1) The F/L flip-flop is cleared using a clear F/L command
  (2) the channel is disabled
  (3) LSB & MSB of the address are programmed
  (4) LSB & MSB of the count are programmed
Once these four operations are performed, the channel is programmed and ready to use.
  additional programming is required to select the mode of operation before the channel is enabled and started
Notes:   if F/L = 0, the low-order byte is selected
  if F/L = 1, the high-order byte is selected

## Slide 139: Programming the 8237
Write a control word in Mode registers
  Select Channel, Type of Transfer (R,W, Verify)
  DMA mode (block, single byte, demand mode)
Write a control word in Command registers
  Priority among channel
  Enable the 8237, DREQ & DACK active level
Write the starting address of the data block to be transferred in the Channel MAR
Write the count in the Channel Count Reg

## Slide 140: Transfer 1K of memory from/ to Floppy disk at CH3
Disable DMA controller & begin initialization Instructions
Initialize CH3
Starting address of Memory Block (Say 4075H) and subsequent bytes are increasing address order
Command parameters: Normal timing, Fixed priority, late write, DREQ&DACK both active low
Set up the demand mode so that DMA can complete the transfer without any interruption

## Slide 141: Program to transfer
MOV AL, 0000100B ; (Disable DMA)
OUT 08H, AL ; Send to Command Reg
MOV AL,00000111V ;00 Demand mode, increAddress,
0 Disable autoload, 01 write, 11=CH3
OUT 0BH, AL ; Send to Mode Reg
MOV AL,04H ; lower Address to
OUT 06H ; MAR CH3
MOV AL,75H ; 7504 Address
OUT 06H, AL
MOV AL,FFH ; lower byte of Tc =03FF, 1K Byte
OUT 07H,AL ; CH3 count Register
MOV AL,03H ; higher byte of 03FF
OUT 07H, AL ; CH3 Count Register
MOV AL, 1000000B ; Command for DACK High
OUT 08H,AL ; Send to command Register
Notes: The address (ex 08) needs to be appended with the CS (address decoding)

## Slide 142: 8251 USART

## Slide 143: Data Comm: Serial Vs Parallel
Serial
  Cheaper
  Slower
Parallel
  Faster
  Data skew
  Limited to small distances
Data Transmission
Parallel
Serial
Synchronous
ASynchronous

## Slide 144: Serial Communication: How ?
Two basic modes of data transmission
Sender
1
1
001001
Receiver
1
1
001001
10010011
Sender
1
1
001001
Receiver
1
1
001001
Parallel to serial
Conversion
Serial to parallel
Conversion
Serial Transmission
Parallel Transmission

## Slide 145: Type of Serial Communication
Synchronous
  Sender and receiver must synchronize
    Done in hardware using phase locked loops (PLLs)
  Block of data can be sent
  More efficient : Less overhead than asynchronous transmission
  Expensive
Asynchronous
  Each byte is encoded for transmission
    Start and stop bits
  No need for sender and receiver synchronization

## Slide 146: Type of Serial Communication
Sender
Sender
Receiver
Receiver
Data
Data
Data
Data
Data
Data
Data
Data
a
Transmission Gaps
Asynchronous transmission
Synchronous transmission
CLK

## Slide 147: Type of Serial Communication
Asynchronous transmission
8 bit Data
Start Bit
Start Bits
1 0 0 0 1 1 1 0
LSB MSB
Time
1 start
bit
1 or 2 Stop
bit
Source data

## Slide 148: Simplex and Duplex Transmission
Simplex
  Data are transmitted in one directions
  Example: CPU to printer
Duplex
  Data flow in both direction
  Half Duplex (Transmission goes on way at a time)
  Full Duplex (Both ways simultaneously)

## Slide 149: Rate of transmission
Rate at which bits are transmitted (BAUD)
Number of signal changes per second
Bit time: how long the Bit stay On or Off
Printer, Terminal Baud Adjustable (50-9600)
1200Baud means: Bit stay for 1/1200=0.83ms

## Slide 150: Error Check
Parity Check
  Even parity: When odd numbers of 1 make D7=1
    Send Even number of 1
  Odd parity: When even number of 1 make D7=1
    Send Odd number of 1
Cyclic Redundancy Code (CRC)
  Synchronous Communication
  Stream of Data can be represented by Cyclic polynomial that divided by a constant polynomial
  Reminder to set Bits and Send out as check for error

## Slide 151: 8251
The 8251A is a programmable serial communication interface chip designed for synchronous and asynchronous serial data communication.
It supports the serial transmission of data.
It is packed in a 28 pin DIP.

## Slide 152: Pin details

## Slide 153: Architecture

## Slide 154: Arch - details
The functional block diagram of 825 1A consists five sections.
They are:
Read/Write control logic
Transmitter
Receiver
Data bus buffer
Modem control.

## Slide 155: Read/Write control logic
The Read/Write Control logic interfaces the 8251A with CPU, determines the functions of the 8251A according to the control word written into its control register.
It monitors the data flow.
This section has three registers and they are control register, status register and data buffer.
The active low signals RD, WR, CS and C/D(Low) are used for read/write operations with these three registers.

## Slide 156: Read/Write control logic
When C/D(low) is high, the control register is selected for writing control word or reading status word.
When C/D(low) is low, the data buffer is selected for read/write operation.
When the reset is high, it forces 8251A into the idle mode.
The clock input is necessary for 8251A for communication with CPU and this clock does not control either the serial transmission or the reception rate.

## Slide 157: Transmitter
If buffer register is empty, then TxRDY is goes to high.
If output register is empty then TxEMPTY goes to high.
The clock signal, TxC (low) controls the rate at which the bits are transmitted by the USART.
The clock frequency can be 1,16 or 64 times the baud rate.

## Slide 158: Receiver
The receiver section accepts serial data and convert them into parallel data
The receiver section is double buffered, i.e., it has an input register to receive serial data and convert to parallel, and a buffer register to hold the parallel data.
When the RxD line goes low, the control logic assumes it as a START bit, waits for half a bit time and samples the line again.
If the line is still low, then the input register accepts the following bits, forms a character and loads it into the buffer register.

## Slide 159: Receiver
The CPU reads the parallel data from the buffer register.
When the input register loads a parallel data to buffer register, the RxRDY line goes high.
The clock signal RxC (low) controls the rate at which bits are received by the USART.
During asynchronous mode, the signal SYNDET/BRKDET will indicate the break in the data transmission.
During synchronous mode, the signal SYNDET/BRKDET will indicate the reception of synchronous character.

## Slide 160: 8251 mode register
7
6
5
4
3
2
1
0
Mode register
Number of
Stop bits
00: invalid
01: 1 bit
10: 1.5 bits
11: 2 bits
Parity
0: odd
1: even
Parity enable
0: disable
1: enable
Character length
00: 5 bits
01: 6 bits
10: 7 bits
11: 8 bits
Baud Rate
00: Syn. Mode
01: x1 clock
10: x16 clock
11: x64 clock

## Slide 161: 8251 command register
TxE: transmit enable
DTR: data terminal ready
RxE: receiver enable
SBPRK: send break character
ER: error reset
RTS: request to send
IR: internal reset
EH: enter hunt mode
TxE
DTR
RxE
SBRK
ER
RTS
EH
IR

## Slide 162: 8251 status register
DSR
SYNDET
FE
OE
PE
TxEMPTY
RxRDY
TxRDY
TxRDY: transmit ready
RxRDY: receiver ready
TxEMPTY: transmitter empty
PE: parity error
OE: overrun error
FE: framing error
SYNDET: sync. character detected
DSR: data set ready

## Slide 163: Initializing the 8251
To implement serial communication the MPU must inform the 8251 about the mode, baud, stop bits, parity etc. A set of control words must be loaded.
  Mode Words
    Specifies general characteristics of the operation.
  Command Words
    Enables the data transmission and/or reception
  Status Word provides the information concerning register status and transmission errors.
Any control word written into the control register after a mode word is interpreted as a command word; that means a command word can be changed anytime, however 8251 should be reset prior to writing a Mode word.
8251 can be reset internally by using the Internal Reset Bit D6.

## Slide 164: 8251 A Serial Communication Interface
The 8251A internally interprets the C/D,RD and WR signals as follow:
Whether the mode, control or sync character register is selected depends on the accessing sequence.
A flowchart of the sequencing is given in Fig.

## Slide 166: Summary: Format of the mode register
What value must be written into the mode control register with baud rate divided by 16, char. Size 16 bits, odd parity, one stop bit ?
------------------------------------
01011110 b = 5Eh

## Slide 167: Format of the control register

## Slide 168: Example 1
A program sequence which initializes the mode register and gives a command to enable the transmitter and begin an asynchronous transmission of 7-bit characters followed by an even-parity bit and 2 stop bits is:
    MOV AL,11111010B
    OUT 51H,AL
    MOV AL,00110011B
    OUT 51H,AL

## Slide 169: 8251 interfaced with 8085

## Slide 170
RS-232C standard